## Slide 1: CZ3006/CSC302 Net-centric computing
Li Mo
School of Computer Engineering, N4-2B-61
limo@ntu.edu.sg
Arrangement
  6 tutorials ( computer networks)
  Week 2, 3, 4, 5, 6, 7(8)
Office hours: Tuesday 3:30-5:30pm

## Slide 2
The performance of a client-server system is influenced by two network factors: the bandwidth of the network (how many bits/sec it can transport) and the latency (how many seconds it takes for the first bit to get from the client to the server). Give an example of a network that exhibits high bandwidth and high latency. Then give an example of one with low bandwidth and low latency.

## Slide 3
A transcontinental fiber link might have many gigabits/sec of bandwidth, but the latency will also be high due to the speed of light propagation over thousands of kilometers.
In contrast, a 56-kbps modem calling a computer in the same building has low bandwidth and low latency.

## Slide 4
A Truck carrying tons of CDs (say 100,000), running between NTU and NUS (say 30mins):
Each CD is of 700M bytes volume,
so 700M * 8 bits * 100,000 / 30 mins = ~300G/s
No latency (almost) ……
1 bit information (maybe 2 bits?)

## Slide 5
Besides bandwidth and latency, what other parameter is needed to give a good characterization of the quality of service offered by a network used for digitized voice traffic?
A uniform delivery time is needed for voice, so the amount of jitter in the network is important. This could be expressed as the standard deviation of the delivery time. Having short delay but large variability is actually worse than a somewhat longer delay and low variability.

## Slide 6
A factor in the delay of a store-and-forward packet-switching system is how long it takes to store and forward a packet through a switch. If switching time is 10 µsec, is this likely to be a major factor in the response of a client-server system where the client is in New York and the server is in California? Assume the propagation speed in copper and fiber to be 2/3 the speed of light in vacuum.

## Slide 7
The speed of propagation is 200,000 km/sec, i.e., 200 meters/µsec. In 10 µsec the signal travels 2 km.
Thus, each switch adds the equivalent of 2 km of extra cable.
So the main question is : where is New York and California? ……
If the client and server are separated by 5000 km, traversing even 50 switches adds only 100 km to the total path, which is only 2%. Thus, switching delay is not a major factor under these circumstances.

## Slide 8
What are two reasons for using layered protocols?
Among other reasons for using layered protocols, using them leads to breaking up the design problem into smaller, more manageable pieces, and layering means that protocols can be changed without affecting higher or lower ones,

## Slide 9
What is the principal difference between connectionless communication and connection-oriented communication?
Connection-oriented communication has three phases. In the establishment phase a request is made to set up a connection. Only after this phase has been successfully completed can the data transfer phase be started and data transported. Then comes the release phase.
Connectionless communication does not have these phases. It just sends the data.

## Slide 10
Compare the delay in sending an x-bit message over a k-hop path in a circuit-switched network and in a (lightly loaded) packet-switched network. The circuit set up time is s sec, the propagation delay is d sec per hop, the packet size is p bits, and the data rate is b bps. Under what conditions does the packet network have a lower delay?
1
2
k-1
det
……
src

## Slide 11
1
2
k-1
det
……
src
With circuit switching,
at t = s the circuit is set up;
at t = s + x /b the last bit is sent;
at t = s + x /b + kd the message arrives.
t = s
t = s + x /b
t = s + x /b + kd

## Slide 12
1
2
k-1
det
……
src
t = x /b + d
With packet switching, the last bit is sent at t = x /b.
To get to the final destination, the last packet must be retransmitted k − 1 times by intermediate routers, each retransmission taking p /b sec, so the total delay is
x /b + (k − 1)p /b + kd.
(k − 1)(p/b + d)
p/b + d
x /b + (k − 1)p /b + kd.
Packet switching is faster if x /b + (k − 1)p /b + kd < t = s + x /b + kd
s > (k − 1)p /b.