## Slide 1: The Data Link Layer

## Slide 2
One of your classmates, Scrooge, has pointed out that it is wasteful to end each frame with a flag byte and then begin the next on with a second flag byte. One flag byte could do the job as well, and a byte saved is a byte earned. Do you agree?
FLAG | Header | Payload | Trailer | FLAG

## Slide 3
If you could always count on an endless stream of frames, one flag byte might be enough. But what if a frame ends (with a flag byte) and there are no new frames for 15 minutes. How will the receiver know that the next byte is actually the start of a new frame and not just noise on the line? The protocol is much simpler with starting and ending flag bytes.

## Slide 4
Can you think of any circumstances under which an open-loop protocol (error-correction code, e.g., a Hamming code) might be preferable to the feedback type protocols discussed throughout this chapter?
If the propagation delay is very long, as in the case of a space probe on or near Mars or Venus, forward error correction is indicated. It is also appropriate, in a military situation in which the receiver does not want to disclose his location by transmitting. If the error rate is low enough that a error correcting code is good enough, it may also be simpler. Finally, real-time systems cannot tolerate waiting for retransmissions.

## Slide 5
A 3000-km-long T1 trunk (1.537 Mbps) is used to transmit 64-byte frames using sliding window protocol 5 (using go-back-n). If the propagation speed is 6 µsec/km, how many bits should the sequence number be (so full channel utilization can be achieved)?
Propagation time is 3000km/(6µsec/km) = 18 ms
Transmission time is 64*8bits/1.537 Mbps = 0.300 msec
Round trip time 18ms + 18ms + 0.3ms = 36.3ms
Allows 121 frames to be transmitted before the 1st ACK
Seven-bit sequence numbers
What about protocol 6?

## Slide 6: The window size
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
(a) Window size = MAX_SEQ
Frame
0-6
ACK
0-6
(b) Window size = (MAX_SEQ+1)/2
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Frame
0-3
ACK
0-3
Old
Frame 0
Old
Frame 0
RIGHT
WRONG

## Slide 7
Frames of 1000 bits are sent over a 1-Mbps satellite channel (with a propagation delay of 270 msec). Acknowledgements are always piggybacked onto data frames. The headers are very short. Three bit sequence numbers are used. What is the maximum achievable channel utilization for
(a) Stop-and-wait.
(b) Protocol 5.
(c) Protocol 6.
Round trip time = 541 ms
542 ms

## Slide 8
Round trip time = 542 ms
Stop-and-wait.
1 frame is sent: 1ms/542ms = 0.18%
(b) Protocol 5.
7 frames are sent: 7ms/542ms = 1.29%
(c) Protocol 6.
4 frames are sent: 4ms/542ms = 0.74%

## Slide 9
In protocol 6, when a data frame arrives, a check is made to see if the sequence number differs from the one expected and NoNak is true. If both conditions hold, an NAK is sent. Otherwise, the auxiliary timer is started. Suppose that the else clause were omitted. Would this change affect the protocol's correctness?
0
0
1
1
8
8
9
9
10
10
2
x
3
3
4
4
5
5
2
2
6
6
7
7
2

## Slide 10
0
0
1
1
2
3
3
2
x
x
x
x
0
0
x
4
x
1
1
2
3
3
2
x
x
x
0
0
1
1
2
3
3
2
x
x
x
x

## Slide 11
In summary, this might lead to deadlock. Suppose machine A is communicating with machine B, and the window size is 4 (MaxSeq = 7). Consider the following scenario:
A has sent B frames 0-3, and B has received all of them, sent back acknowledgements, and shifted its receiving window to wait for frames 4-7. Under the following conditions, the protocol fails:
If all acknowledgements got lost, A will timeout and retransmit frame 0. B will reject this duplicated frame 0, and send back a Nak.
If the Nak also got lost, A will go on retransmitting frames 1-3. But B will reject all these duplications WITHOUT sending back a Nak any more since NoNak has been set to false.
If there is NO reverse traffic from B to A, A will keep retransmitting frames 0-3, but B will keep rejecting them for ever !
Setting the auxiliary timer results in a correct acknowledgement being sent back eventually instead, which resynchronizes.