## Slide 1: The MAC Sublayer and LAN

## Slide 2
Consider building a CSMA/CD network running at 1 Gbps over a 1-km cable with no repeaters. The signal speed in the cable is 200,000km/sec. What is the minimum frame size?

## Slide 3: Collision Detection Time and Minimal Frame Length
A
B
At time 0, A sends out one frame.
At time  - ε, the frame almost arrives at B.
At the same time, B sends out one frame.
B detects the collision immediately (at time  – ε).
The frame from B arrives at A at time 2.
A detects the collision (at time 2).

## Slide 4
For a 1-km cable, the one-way propagation time is 5 µsec, so 2τ = 10 µsec. To make CSMA/CD work, it must be impossible to transmit an entire frame in this interval. At 1 Gbps, all frames shorter than 10,000 bits can be completely transmitted in under 10 µsec, so the minimum frame is 10,000 bits or 1250 bytes.

## Slide 5
Ethernet frames must be at least 64 bytes long to ensure that the transmitter is still going in the event of a collision at the far end of the cable. Fast Ethernet has the same 64-byte minimum frame size but can get the bits out ten times faster. How is it possible to maintain the same minimum frame size?
The maximum wire length in fast Ethernet is 1/10 as long as in Ethernet.

## Slide 6
3. Suppose that an 11-Mbps 802.11b LAN is transmitting 64-byte frames back-to-back over a radio channel with a bit error rate of 10-7. How many frames per second will be damaged on average?
A frame contains 512 bits. The bit error rate is p = 10−7. The probability of all 512 of them surviving correctly is (1 − p)512, which is about 0.9999488. The fraction damaged is thus about 5 × 10−5. The number of frames/sec is 11 × 106 /512 or about 21,484. Multiplying these two numbers together, we get about 1 damaged frame per second.

## Slide 7
4. Give two reasons why networks might use an error-correcting code instead of error detection and retransmission.
One reason is the need for real-time quality of service. If an error is discovered, there is no time to get a retransmission. The show must go on. Forward error correction can be used here.
Another reason is that on very low quality lines (e.g., wireless channels), the error rate can be so high that practically all frames would have to be retransmitted, and the retransmission would probably damaged as well. To avoid this, forward error correction is used to increase the fraction of frames that arrive correctly.